## Slide 1: Carbon, Nitrogen, and Organic Matter
SOIL 4234 Laboratory No. 7

## Slide 2: Organic Matter: Importance
Complex and chelate metals
Serves as source of nutrients to plants and microorganisms
Contributes to CEC
Aggregate soils

## Slide 3: Techniques for measuring OM/OC
Dry Combustion
  Loss on ignition using a kiln or muffle furnace
  High temperature dry combustion using an automated analyzer
Wet Combustion
Visible Near Infrared Spectroscopy

## Slide 4: Dry Combustion: Loss on Ignition
Organic carbon oxidizes to CO2 and H2O
Mass loss
Problems with gypsum clays
Carbonates – pre treatment to remove carbonates

## Slide 5: Dry Combustion: High Temp - LECO
Total C (%) =
(g CO2 (sample) – g CO2 (blank)
g of dry soil
x 0.2727 x 100
Organic matter (%) = 0.35 + [1.80 x percent organic carbon]

## Slide 6: Wet Combustion: Walkey-Black Method
Potassium dichromate (K2Cr2O7) is mixed with the soil and concentrated H2SO4 is then added.
K2Cr2O7 + H2SO4
→ H2Cr2O7 + K2SO4 + excess H2SO4
Oxidizes organic carbon
CO2 + chromous sulfate (Cr2(SO4)3

## Slide 7: Visible Near Infrared Spectrometry
Uses visible and near-infrared reflectance values
400 nm to about 750 nm
750 nm to about 950 nm

## Slide 8: Soils in Oklahoma
Most N is present in organic nitrogen in the soil organic matter
For every 1% OM = 1000 lbs/acre of N
Approximately 98% of the soil N is unavailable for plant uptake
OM is resistant to further decay

## Slide 9: C:N Ratio
Microorganisms require mineral N – N release from OM
Microorganisms get their carbon from decaying organic matter
Nitrogen availability
  Relative amount of C and N in the OM
  Resistance to decay
  Environmental conditions – microbial activity

## Slide 10: C:N Ratio
C:N Ratio
N not released
OM become resistant to decay
MO die off
More mineral, less MO

## Slide 11: C:N Ratio
C:N Ratio
20:1 or less – mineralization
20:1 or more - immobilization

## Slide 12: Dry Combustion: Loss on Ignition
Soil sample
Crucibles
Tongs
Weighing scale
Oven
Muffle Furnace
Materials needed

## Slide 13: Dry Combustion: Loss on Ignition
  Determine soil sample weight (wet weight)
  Oven dry = 125oC overnight
  Weigh soil samples (dry weight)
  Place dry sample in a muffle furnace
  Burn soil samples at 400oC for 8 to 16 hours
  Weigh burned samples (burned weight)
When soil is heated to high temperatures the organic portion oxidizes to CO2 and H2O but the majority of soil minerals are left intact.

## Slide 14: Dry Combustion: Loss on Ignition
Advantages | Disadvantage
Inexpensive Easy to perform with minimal equipment Uses no chemical | Weight loss can be due to something other than SOM* Rarely applied to low fertility soils for SOM
* Gypsum, montmorillonite, vermicite, and gibbsite - moisture losses of 20-30% of total weight at temperature used for OM oxidation
* Calcareous soil – loss of free carbonates = no distinction between carbonate loss and OC oxidized

## Slide 15: Dry Combustion: Automated Analyzer
Soil sample
Materials needed
LECO automated analyzer

## Slide 16: Nitrogen
Amount of Total Nitrogen present in the soil is also measured.
How is this different from Nitrogen previously measured?
  Includes organic and inorganic forms of nitrogen
Inorganic N
      Ammonia (NH3)
      Ammonium (NH4+)
      Nitrite (NO2-)
      Nitrate (NO3-)
Organic N
  Nitrogen in the form of proteins, nucleic acids found in microbes and organic matter compounds