## Slide 1: Soil Test for Nitrogen
Soil 4234 Lab

## Slide 2: Why Nitrogen?
Required in highest amounts for many crops
Contributes to majority of fertilizer cost for producers

## Slide 4: Nitrogen
Fluctuate due to moisture and mobility in the soil profile
This is why sampling closest to N application is required

## Slide 5: Soil test analysis for Nitrogen
Flow Injection Analysis System
  LACHAT QuickChem 8500
Extractor is KCl
  K+
    Strong enough base to remove NH4+ from any bonding sites
  Cl-
    Strong enough acid to remove NO3-

## Slide 6: Soil test analysis for Nitrate NO3-
Sample Injected
Reduced from NO3- to NO2- in Cd column
Coloring reagent mixed and given certain time to develop
Color is read through sensor, through a 520 nm filter, information is then processed by computer

## Slide 7: Soil Test Analysis for Ammonium NH4+
Sample Injected
Multiple Reactions

## Slide 8
The height of the absorbence curve denotes the concentration of the solution pushed through the Sensor
These values can then be used to calculate the amounts of nutrients found in the extractants.

## Slide 9: N Losses in soil
If we look at our N cycle again…

## Slide 11: N Losses in soil
If we look at our N cycle again…
4 Avenues of losses:
  Leaching
  Plant Loss
  Volatilization
  Denitrification

## Slide 12: N Losses in soil
If we look at our N cycle again…
4 Avenues of losses:
  Leaching: talked about in mobility lab, how its prone to leaching
  Plant Loss
  Volatilization
  Denitrification

## Slide 13: N Losses in soil
If we look at our N cycle again…
4 Avenues of losses:
  Leaching
  Plant Loss: can’t control
  Volatilization
  Denitrification

## Slide 14: N Losses in soil
If we look at our N cycle again…
4 Avenues of losses:
  Leaching
  Plant Loss
  Volatilization
  Denitrification: Occurs in waterlogged soils, so by keeping well drained soils

## Slide 15: N Losses in soil
If we look at our N cycle again…
4 Avenues of losses:
  Leaching
  Plant Loss
  Volatilization
  Denitrification

## Slide 16: N Volatilization
Volatization is the process of NO3-N undergoing chemical reaction to become NH3 gas
We can see that this reaction provides its own basicity for reaction to occur, even in centralized locations

## Slide 17: Objective
To determine NO3- and NH4+ concentrations from soil samples
To understand how soil chemical and physical characteristics affect N volatilization